## Slide 1
BOOM
PROCESSOR

## Slide 2
ISA
02
05
DATAPATH
03
REGISTER STRUCTURE
01
PIPELINE
FEATURES AND REFERENCES
04
DESKTOP PROCESSOR

## Slide 3
Introduction to BOOM ISA
  Berkeley Out-of-Order Machine (BOOM) is a high-performance, out-of-order processor based
on RISC-V ISA.
  It is an open-source core implemented in Chisel and derived from the Rocket Chip
generator.
  Supports 64-bit RISC-V ISA (RV64IMAFD):
I – Integer instructions
M – Multiplication & Division
A – Atomic operations
F – Single-precision floating-point
D – Double-precision floating-point
  Optional extensions: C (Compressed), V (Vector), B (Bit Manipulation)
01
CB.SC.U4CSE23537

## Slide 4
ISA Features
  Execution Modes: Supports User (U), Supervisor (S), and Machine (M) modes.
  Memory Management: Uses Sv39/Sv48 virtual memory, supports TLB (Translation Lookaside Buffer).
  Pipeline Execution:
1.Multi-stage, superscalar pipeline with out-of-order execution.
2.Dynamic scheduling and branch prediction for higher performance.
  Comparison with Rocket Core:
1. BOOM: Out-of-order, high-performance
2. Rocket: In-order, simpler design
01
CB.SC.U4CSE23537

## Slide 5
Registers
  Number & Width: 32 registers (x0 to x31), 64 bits each
  Purpose: Store integer data, addresses, and temporary values
  Key Registers:
    x0: Always holds 0 (zero register)
    x1 (ra): Return address register
    x2 (sp): Stack pointer
    x10 - x17 (a0 - a7): Function arguments and return values
02
General-Purpose Registers:
Floating-Point Registers:
  Number & Width: 32 registers, 64 bits each
  Purpose: Store floating-point values (single and double precision)
CB.SC.U4CSE23566

## Slide 6
Registers
  Purpose: Manage exceptions, interrupts, privilege levels, and performance monitoring
  Key CSRs:
    mstatus: Processor state and interrupt enable bits
    mcause: Cause of the last exception
    cycle and instret: Performance counters
02
Control and Status Registers
Register Renaming and Reorder Buffer
  Purpose: Avoids data hazards (e.g., Write-After-Write (WAW) and Write-After-Read (WAR))
  Hazard Mitigation:
    Structural Hazards: Multiple read/write ports
    Data Hazards: Resolved using forwarding
    Control Hazards: Managed with branch prediction
CB.SC.U4CSE23566

## Slide 7
03
Datapath
FRONT-END: Fetches instructions, decodes them, and prepares instruction for execution.
EXECUTION UNITS: Handles arithmetic, memory access, and floating-point operations.
LOAD/STORE UNITS: Manages memory operations efficiently with store buffers and forwarding
CB.SC.U4CSE23520

## Slide 8
Datapath Components
03
Front-end (Instruction Fetch & Decode)
Execution Units (EUs)
Load/Store Unit
  Uses Branch Prediction Unit (BPU) for fast instruction flow.
  Fetch Buffer (32 entries) holds instructions before decoding.
  Execution Units (ALUs, FPUs, IMUL, AGUs) handle different instructions.
  Reorder Buffer (ROB) (128 entries) maintains program order.
  Distributed Scheduler assigns operations to execution units.
  L1 Data Cache (32 KiB, 8-way) stores frequently accessed data.
  Load & Store Queues manage memory operations.
CB.SC.U4CSE23520

## Slide 9
03
Datapath
CB.SC.U4CSE23520

## Slide 10
Datapath Components
03
Front-end (Instruction Fetch & Decode)
  Instruction Fetching – The L1 Instruction Cache (32 KiB, 8-way set associative) fetches 16 Bytes per cycle, ensuring a high-speed supply of instructions.
  Branch Prediction – It minimizes pipeline stalls using the BTB (1-cycle redirect), Gshare BPU (3-cycle redirect), and Return Address Stack (RAS).
  Instruction Buffering – The Fetch Buffer (32 entries) temporarily holds instructions before they enter the decode stage.
  Decoding – The 4-wide Decode Unit processes four instructions per cycle, translating them into micro-operations (μOPs) for execution.
CB.SC.U4CSE23520

## Slide 11
Datapath Components
03
Execution Units (EUs)
  Instruction Scheduling – The Reorder Buffer (ROB, 128 entries) manages renaming, allocation, and retirement of instructions to maintain execution order.
  Issue Queues – Instructions are dispatched to FP Issue Queue, INT Issue Queue, and MEM Issue Queue (each with 32 entries) for execution.
  Execution Units – Includes ALUs for integer operations, FPUs for floating-point computations, IMUL for multiplication, FDIV for division, and AGUs for memory address calculations.
  Out-of-Order Execution – The processor dynamically schedules instructions to maximize throughput and minimize stalls.
CB.SC.U4CSE23520

## Slide 12
03
Datapath
CB.SC.U4CSE23520

## Slide 13
Datapath Components
03
Load/Store Unit
  Memory Access – The L1 Data Cache (32 KiB, 8-way set associative) processes 8 Bytes per cycle, improving data access speeds.
  Load/Store Queues – Instructions enter the Load Queue (32 entries) and Store Queue (32 entries) before memory operations are executed.
  Store Buffering & Forwarding – Enables stores to be processed without waiting for memory, reducing write latencies.
  Cache Miss Handling – Line Fill Buffers (10 entries) and 8 Miss Status Holding Registers (MSHRs) manage cache misses and data prefetching.
CB.SC.U4CSE23520

## Slide 14
The Boom Pipeline
01
04
Fetch
  Instructions are fetched from instruction memory and pushed into a FIFO queue, known as the Fetch Buffer .
  Branch prediction also occurs in this stage.
02
Decode
  Decode pulls instructions out of the Fetch Buffer and generates the appropriate Micro-Op(s) (UOPs) to place into the pipeline.
03
Rename
  The ISA, or “logical”, register specifiers (e.g. x0-x31) are then renamed into “physical” register specifiers.
CB.SC.U4CSE23542

## Slide 15
The Boom Pipeline
05
Issue
04
  UOPs sitting in a Issue Queue wait until all of their operands are ready and are then issued.
  This is the beginning of the out–of–order piece of the pipeline.
06
Register Read
  Issued UOPs s first read their register operands from the unified Physical Register File (or from the Bypass Network)…
04
Dispatch
  The UOP is then dispatched, or written, into a set of Issue Queue s.
CB.SC.U4CSE23542

## Slide 16
04
The Boom Pipeline
CB.SC.U4CSE23542

## Slide 17
The Boom Pipeline
07
08
04
Execute
Memory
  The Execute stage is where the functional units reside.
  Issued memory operations perform their address calculations in the Execute stage, and then store the calculated addresses in the Load/Store Unit which resides in the Memory stage.
  The Load/Store Unit consists of three queues: a Load Address Queue (LAQ), a Store Address Queue (SAQ), and a Store Data Queue (SDQ).
  Loads are fired to memory when their address is present in the LAQ.
CB.SC.U4CSE23542

## Slide 18
The Boom Pipeline
04
09
Write back
10
Commit
  ALU operations and load operations are written back to the Physical Register File.
  The Reorder Buffer (ROB), tracks the status of each instruction in the pipeline.
  When the head of the ROB is not-busy, the ROB commits the instruction.
  For stores, the ROB signals to the store at the head of the Store Queue (SAQ/SDQ) that it can now write its data to memory.
CB.SC.U4CSE23542

## Slide 19
Features
  Description: Instructions execute as soon as their operands are ready, rather than in strict program order.
  Benefit: Increases throughput and minimizes idle time by improving instruction parallelism.
05
Out-of-Order Execution (OOE)
Superscalar Execution
  Description: BOOM can execute multiple instructions per clock cycle using multiple functional units.
  Benefit: Enhances processor performance by increasing instruction-level parallelism.
Branch Prediction
  Description: Predicts the outcome of branches to avoid pipeline stalls due to control hazards.
  Implementation: Uses advanced predictors to improve accuracy.
  Benefit: Keeps the pipeline full, reducing performance loss from mispredicted branches.
CB.SC.U4CSE23566

## Slide 20
Features
  Description: Supports multi-level instruction and data caches (L1, etc.) to optimize memory access.
  Benefit: Reduces memory latency and improves overall performance.
05
Cache Hierarchy
Scalability and Configurability
  Description: BOOM is highly customizable in terms of pipeline depth, cache size, branch predictors, etc.
  Benefit: Allows scaling up or down for different performance and resource requirements.
  Use Case: Used in research, academic studies, and chip design due to open-source nature
CB.SC.U4CSE23566

## Slide 21
References
  Berkeley Architecture Research. "BOOM: An Open-Source Out-of-Order RISC-V Core." (https://boom-core.org)
  Patterson, David A., and John L. Hennessy. Computer Organization and Design RISC-V Edition.
  Git Hub Repository: https://github.com/riscv-boom/riscv-boom
  Technical Report Paper: The Berkeley Out-of-Order Machine (BOOM): An Industry- Competitive, Synthesizable, Parameterized RISC-V Processor.
https://www2.eecs.berkeley.edu/Pubs/TechRpts/2015/EECS-2015-167.pdf
05
CB.SC.U4CSE23566

## Slide 22
THANK YOU
TEAM MEMBERS:
CB.SC.U4CSE23520
CB.SC.U4CSE23542
CB.SC.U4CSE23566
CB.SC.U4CSE23537